## Slide 1: StressThermal
A multidimensional simulation environment for IC interconnect reliability analysis
ANALYSIS MODES
Mechanics
∇·σ + b = 0
Quasistatic force equilibrium
Solve for: displacement field u
Thermal
ρcₚ ∂T/∂t − ∇·(k∇T) = Q
Heat equation
Solve for: temperature field T
COUPLED ANALYSIS
Thermomechanical
Thermal expansion
Thermal → Mechanics
Δεᵗʰ ≈ αᵣₑₗ(T̄) ΔT I
Thermal → Mechanics
C = C(T)
Electrothermal
Joule heating · temperature-dependent conductivity
Electrical current → Thermal
Q = J꜀·E = σₑ(T)|E|²
Electromechanical
Inverse piezoelectric effect
Electrical analysis → Mechanics
σⱼᵖ = −Σᵢ eᵢⱼ (Eᵢⁿᵉʷ − Eᵢᵒˡᵈ)
NUMERICS
Spatial discretization
FEM · Mechanics
FVM · Thermal / Electrical
Time integration
TRBDF
Nonlinear solution
Newton method
Linear solvers
Direct · Iterative
Electrical analysis
Electrical current
Electrostatic
∇·(σₑ∇φ) = ∇·Jᴅ
Jᴅ = −∂(ε∇φ)/∂t
Current Laplace equation
∇·(ε∇φ) = −ρf
Poisson equation in dielectrics
Solve for: electric potential φ, then derive electric field E = −∇φ
Thermal → Electrical current
T → σₑ(T) → re-solve electric potential φ
E = −∇φ; J꜀ = σₑ(T)E
Temperature-dependent mechanical properties
LCA
Alpha
TODO
Alpha
TODO
TODO
TODO
→
Prototype
→
Alpha
→
Beta
→
LCA
Notes: 本次汇报将分为五个部分。首先，我们将明确TCAD的基础定位和核心价值。其次，将重点分析TCAD在半导体、量子计算和可控核聚变这三大未来赛道中所发挥的全局性作用。接着，我们会探讨TCAD在产学研联动中的价值。然后，通过国际经验教训，阐述自主可控EDA/TCAD的重要性。最后，将以国产企业为例，展望我国EDA生态的构建与未来启示。

## Slide 2: Mechanics
Mature mechanics capabilities with extensive nonlinear analysis
Rich material models, elements, stress-causing mechanisms and boundary conditions
Analysis methods
Material models
Element library
Stress-causing mechanisms
Nonlinear analysis
Boundary conditions & constraints
Triangle
Quadrilateral
Tetrahedron
Hexahedron
CSSE
Beam
Mode 1
Mode 2
Mode 3
Quasistatic equilibrium
How does it deform
under slowly applied loads?
Linear buckling
At what load and in what
shape does it buckle?
Post-buckling
How does it deform and
carry load after buckling?
LCA
TODO
TODO
LCA
TODO
LCA
TODO
Alpha
TODO
Elastic
LCA
Isotropic / anisotropic
(cubic, hexagonal, orthotropic)
Viscous & viscoelastic
LCA
Viscous · Maxwell · standard linear solid
Plastic & viscoplastic
Alpha
Incremental / deformation plasticity · Anand
Power-law creep
Prototype
Bailey–Norton · Mukherjee–Bird–Dorn
Swelling
Prototype
Cohesive damage / softening
Prototype
Temperature-dependent material parameters
LCA
Continuum elements
Plane strain · 3D solid
LCA
Plane stress
TODO
Axisymmetric
TODO
Composite solid shell
Alpha
Structural elements
3D Timoshenko
composite beam
TODO
Interpolation
First / second order
LCA
Mixed mesh
TODO
Thermal mismatch · intrinsic stress
LCA
Densification
TODO
Grain growth
TODO
Gravity force
Prototype
Surface reflow force
TODO
Edge dislocation
TODO
Inverse piezoelectric effect
TODO
Fluid surface tension / pressure
TODO
Cohesive zipping force
TODO
Phase change
TODO
Etch / deposition stress rebalancing · etc.
LCA
Geometric nonlinearity
Large deformation and rotation
LCA
Boundary & interface nonlinearity
Mechanical contact
TODO
Crack analysis
TODO
Material nonlinearity
see material models
Prescribed displacement
LCA
Displacement rate · traction · pressure
LCA
Point force
LCA
Moment · symmetry
Alpha
Periodic boundary condition
Alpha
Coupling boundary condition
Alpha
Beam-plate coupling
Alpha
Variable boundary conditions
Alpha
Notes: 本次汇报将分为五个部分。首先，我们将明确TCAD的基础定位和核心价值。其次，将重点分析TCAD在半导体、量子计算和可控核聚变这三大未来赛道中所发挥的全局性作用。接着，我们会探讨TCAD在产学研联动中的价值。然后，通过国际经验教训，阐述自主可控EDA/TCAD的重要性。最后，将以国产企业为例，展望我国EDA生态的构建与未来启示。

## Slide 3: Thermal
Comprehensive thermal physics support
Steady-state & transient · conduction, convection and radiation
Analysis methods
Alpha
Steady-state · Transient
Heat transfer mechanisms
Alpha
Conduction
Heat flow within and between materials
Convection
Heat exchange with a surrounding liquid or gas
Radiation
Radiative heat exchange with the environment
Material properties
Alpha
Thermal conductivity
Isotropic / anisotropic
(orthotropic, aligned with X / Y / Z)
Heat storage
Mass density ρ · specific heat capacity cₚ
cₚ is per unit mass; ρcₚ is heat capacity per unit volume
Surface emission
Emissivity
Temperature-dependent material parameters
Volumetric heat generation
Alpha
Applied heating
Volumetric power density
Electrical heating
Joule heating in conducting materials
Boundary & interface conditions
Thermal boundary conditions
Prescribed temperature
Alpha
Temperature ramps
Alpha
Prescribed heat flux
Alpha
Contact power
Alpha
Adiabatic boundary (insulated): zero normal heat flux
Alpha
Ambient heat exchange
Convection
Alpha
Radiation
Alpha
Thermal resistor
Prototype
Material interfaces
Temperature / flux continuity
Prototype
Interface thermal resistance
Prototype
Notes: 本次汇报将分为五个部分。首先，我们将明确TCAD的基础定位和核心价值。其次，将重点分析TCAD在半导体、量子计算和可控核聚变这三大未来赛道中所发挥的全局性作用。接着，我们会探讨TCAD在产学研联动中的价值。然后，通过国际经验教训，阐述自主可控EDA/TCAD的重要性。最后，将以国产企业为例，展望我国EDA生态的构建与未来启示。

## Slide 4: Case 1 — Package thermomechanical reliability
Geometry
Temperature
Equivalent stress
Temperature
Mapping
Case background
Power-device package (adapted from PowerSO-10RF / LDMOS)
Uneven heating → expansion mismatch → stress
Thermal · Highlighted feature
Mechanics · Highlighted feature
Steady-state
Conduction · convection
Radiation
Quasistatic equilibrium
Thermal mismatch
Prescribed displacement
ACCURACY
PERFORMANCE
Time (s)
StressThermal
Golden tool - S
Golden tool - A
Thermal solve
4.25
2.30
8.30
Mechanics solve
7.07
4.24
10.00
82,477 solid tetrahedra · 15,653 solid vertices
Metric
StressThermal
Golden tool - S
Golden tool - A
Maximum Temperature
(K)
Maximum Equivalent
Stress (MPa)
490.016
489.456
489.433
1105.175
1105.423
1106.836
Source: adapted from Sentaurus Applications Library
Solver: StressThermal
Post-processing: h5py · NumPy · VTK · Pillow
Notes: 本次汇报将分为五个部分。首先，我们将明确TCAD的基础定位和核心价值。其次，将重点分析TCAD在半导体、量子计算和可控核聚变这三大未来赛道中所发挥的全局性作用。接着，我们会探讨TCAD在产学研联动中的价值。然后，通过国际经验教训，阐述自主可控EDA/TCAD的重要性。最后，将以国产企业为例，展望我国EDA生态的构建与未来启示。

## Slide 5: Case 2 — Submodelling
Source: adapted from Sentaurus Applications Library
Solver: StressThermal
Post-processing: h5py · NumPy · VTK · Pillow
Geometry
3 × 3 pillar array
Single-pillar submodel
Equivalent stress
Equivalent stress
Global-to-local displacement
Mapping
Case background
Flip-chip package · 3 × 3 copper pillars
Cooling: 180 °C → 25 °C
Highlighted feature: Mechanical submodelling
Map global displacement
Refine the single-pillar mesh
Solve local stress
ACCURACY
Maximum Equivalent
StressThermal
Golden tool - S
Golden tool - A
Global
887.678
887.678
887.678
Local
703.701
703.701
703.700
PERFORMANCE
Time (s)
StressThermal
Golden tool - S
Golden tool - A
Global solve
16.69
16.45
38.60
Local solve
43.02
39.10
77.50
Global: 246,681 tets · Local: 422,904 tets
Stress (MPa)
Notes: 本次汇报将分为五个部分。首先，我们将明确TCAD的基础定位和核心价值。其次，将重点分析TCAD在半导体、量子计算和可控核聚变这三大未来赛道中所发挥的全局性作用。接着，我们会探讨TCAD在产学研联动中的价值。然后，通过国际经验教训，阐述自主可控EDA/TCAD的重要性。最后，将以国产企业为例，展望我国EDA生态的构建与未来启示。

## Slide 6: Future plans
From physics features to integrated solutions
TODO FEATURES
Mechanics
Buckling
GT-S / GT-A
Crack analysis
GT-S / GT-A
Contact analysis
GT-S / GT-A
Electrical Analysis
Electrical current
GT-S / GT-A
Electrostatic
GT-S / GT-A
Electrical Related
Coupling
Electromechanical
GT-S / GT-A
Electrothermal
GT-S / GT-A
SOLUTIONS & APPLICATIONS
Hybrid Bonding
GT-S / GT-A
A next-generation solution for high-density,
low-power chip-to-chip integration.
Existing foundation
Stress analysis
Planned extensions
Mechanical contact
Crack analysis
Cohesive damage / softening
Vibration Analysis
GT-A only
Chip / package / PCB reliability
Identify package / PCB resonance
Existing foundation
Stress analysis
Planned extensions
Frequency / Modal
Harmonic Response
Response Spectrum
Trace Mapping
GT-A only
ECAD copper layout → FE material properties
1 Source fraction
2 Target FE mesh
3 Mapped fraction
Source: GT-A reference guide · 2025 R1
Existing foundation
Stress analysis
Thermal analysis
Planned extensions
ECAD import & alignment
Copper-fraction source grid
Grid–FE overlap weighting
Effective material properties
Risks & gaps
GT = Golden Tool
01 Reference
Follows GT-S; GT-A coverage limited.
GT-A has higher market share.
02 Thermal analysis numerics
GT-S: FVM / GT-A: FEM
Separate validation needed.
03 User adoption
GT-S / GT-A input styles
Learning & migration barriers.
04 Pre/post-processing
Only solver core available;
pre/post-processing needed.
Notes: 本次汇报将分为五个部分。首先，我们将明确TCAD的基础定位和核心价值。其次，将重点分析TCAD在半导体、量子计算和可控核聚变这三大未来赛道中所发挥的全局性作用。接着，我们会探讨TCAD在产学研联动中的价值。然后，通过国际经验教训，阐述自主可控EDA/TCAD的重要性。最后，将以国产企业为例，展望我国EDA生态的构建与未来启示。

## Slide 7: Mechanics & Thermal
Shared capabilities · Backup
Data interfaces
Multiscale modeling · Submodeling
Data import
External mesh import (supports GFR and DF-ISE)
Field import to resume simulations (GFR)
Results output
Field results (GFR)
Probe / profile results (X–Y tables)
Supported output fields
Mechanics
Displacement · displacement increments · pseudo displacement
Stress components · von Mises stress · pressure
Principal stresses / strains · principal directions
Elastic / plastic / viscoplastic / creep / swelling strain
Equivalent plastic / viscoplastic / creep strain
Strain energy densities · energy-rate densities
Nodal forces · reaction forces
Stress / strain maxima · etc.
Thermal
Temperature · previous temperature · temperature gradient
Heat flux · total heat-source density · Joule heating
Derived hotspot maps · etc.
Coarse global response → refined local detail
3 × 3 copper-pillar array
Single-pillar submodel
→
180 → 25 °C · Equivalent stress · 0–600 MPa
Source: CopperPillar_FlipChip_Crack · vendor-run submodel adaptation
Interpolate global fields onto local outer boundaries
Mechanics: displacement increments → local stress
Thermal: temperature → local temperature / heat flow
Notes: 本次汇报将分为五个部分。首先，我们将明确TCAD的基础定位和核心价值。其次，将重点分析TCAD在半导体、量子计算和可控核聚变这三大未来赛道中所发挥的全局性作用。接着，我们会探讨TCAD在产学研联动中的价值。然后，通过国际经验教训，阐述自主可控EDA/TCAD的重要性。最后，将以国产企业为例，展望我国EDA生态的构建与未来启示。